## Slide 1
Layerweaver: Maximizing Resource Utilization of Neural Processing Units via Layer-Wise Scheduling
Young H. Oh† , Seonghak Kim*, Yunho Jin*, Sam Son*, Jonghyun Bae* Jongsung Lee*, Yeonhong Park*, Dong Uk Kim*, Tae Jun Ham*, Jae W. Lee*
The 27th IEEE International Symposium on High-Performance Computer Architecture
*Seoul National University
†Sungkyunkwan University

## Slide 2: Neural Processing Units for Clouds
Hardware resources in Neural Processing Units (NPUs)
  Computing units (TOP/s), On-chip buffers (MB), Off-chip memory bandwidth (GB/s)
Compute-to-Memory Bandwidth Ratio varies widely among NPUs
  According to target applications (Training or Inference), service scenarios, area budget, etc.
Chart: Off-chip Memory Bandwidth (GB/s)
| 34 | 0.127 | 68 | 102.4 | 102 | 100
Inference | 92 | 0.042 | 92 | 166.4 | 20 | 128
Training | 90 | 45 | 119
General Purpose | 142 | 35.6 | 156 | 198 | 312

## Slide 3: Characteristics of DNN Models
Arithmetic Intensity (Ops/Byte):
  How many compute operations are performed per byte loaded from off-chip DRAM
The metric is determined by:
  Type of Layer: Convolution >> Depth-wise Convolution > Matrix Multiply > Embedding Lookup
  Batch Size: Large batch > Small batch
Off-chip DRAM
Off-chip DRAM
Off-chip DRAM
Off-chip DRAM
Low Reuse, Relatively
Frequent New Data Fetch
Low Arithmetic Intensity
Off-chip DRAM
Off-chip DRAM
Off-chip DRAM
Off-chip DRAM
Infrequent data fetch
High Arithmetic Intensity
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
Shared Buffer
High Batch Convolution, Depth-wise Convolution, etc.
Low Batch Matrix Multiplication,
Embedding Lookup, etc.
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
PE
Array
Shared Buffer
High Reuse, Relatively
Many Operations with Data

## Slide 4: NPU Resource Underutilization Problem
NPU Capabilities
DNN Model Characteristics
Throughput (TOP/s)
Memory Bandwidth (GB/s)
Global Shared Buffer
PE
PE
PE
PE
PE
PE
PE
PE
PE
Off-chip DRAM
Compute-bound (e.g. CNNs)
High Arithmetic Intensity
Memory-bound (e.g. NLP)
Low Arithmetic Intensity
Arithmetic
Intensity
Compute to Memory
Bandwidth Ratio
Should be balanced for high resource utilization
≈
We need to close this gap between compute-to-memory bandwidth ratio (NPU) and arithmetic intensity (DNN model) to achieve high utilization.

## Slide 5: NPU Resource Underutilization Problem
No one-size-fits-all NPUs for various DNN models and batch sizes
  Compute-centric accelerators are well-suited for Vision Tasks
  Memory-centric accelerators prefers NLP & Recommendation Tasks
Significant mismatch between Arithmetic Intensity and Compute-to-Memory BW ratio
Chart: Batch Size
| 1 | 2 | 4 | 8 | 16
BB | 15.7961 | 29.6013 | 59.1855 | 118.345 | 378.4985
BL | 15.7598 | 29.5404 | 59.0715 | 118.1284 | 377.9415
NCF | 25.1452 | 25.1452 | 25.1452 | 25.1452 | 37.7056
XL | 15.7783 | 29.5803 | 59.1573 | 118.3092 | 378.5737
IC | 400.8794 | 801.6282 | 1603.1014 | 3206.0654 | 6412.0241
MN | 873.2481 | 1745.6301 | 3490.444 | 6980.0319 | 13959.4814
RN | 259.4243 | 518.6236 | 1037.0232 | 2073.8245 | 4147.5046
RX | 856.0349 | 1711.8334 | 3423.4449 | 6846.6606 | 13693.1672
TPUv3 | 100 | 100 | 100 | 100 | 100
NNP-I | 1352.9412 | 1352.9412 | 1352.9412 | 1352.9412 | 1352.9412
Eyeriss | 330.7087 | 330.7087 | 330.7087 | 330.7087 | 330.7087
Cambricon | 1250 | 1250 | 1250 | 1250 | 1250
TPUv3
Eyeriss
Goya
NNP-I
Cambricon
Comp-centric
Mem-centric
* Each acronym corresponds to BERT-base (BB), BERT-large (BL), NCF recommendation (NCF), XLNet (XL), InceptionV3 (IC), MobileNetV2 (MN), ResNet50 (RN), ResNeXt50 (RX)
…
Longer compute time
TPUv3
…
Longer memory access time
Arithmetic Intensity < Comp. to MemBW Ratio
Arithmetic Intensity > Comp. to MemBW Ratio
Compute Util.
Memory Util.
Time
Compute Util.
Memory Util.

## Slide 6: NPU Resource Underutilization Problem
This mismatch leads to Resource Underutilization
  Conventional way: Double-Buffering / Decoupled Access-and-Execution (Prefetching)
Imbalance between NPU and DNN models
Time
DRAM Channel Idle Time
Compute Idle Time
Double-buffering or Prefetching
Compute Util.
Memory Util.
Mem-intensive Model
Comp-intensive Model
Mem-intensive Model
Comp-intensive Model

## Slide 7: NPU Resource Underutilization Problem
This mismatch leads to Resource Underutilization
  Conventional way: Double-Buffering / Decoupled Access-and-Execution (Prefetching)
  Problem: Sub-optimal scheduling as interleaving over the model boundary is not allowed
Time
Large benefits w/ time-multiplexing
DRAM Channel Idle Time
Compute Idle Time
Mem-intensive Model
Comp-intensive Model
Double-buffering or Prefetching
Compute Util.
Memory Util.
Layer-wise
Interleaving
Compute Util.
Memory Util.
  Our Proposal: Layer-wise interleaving for balanced resource utilization
  Challenge: Finding a proper prefetch timing is non-trivial due to limited on-chip buffers

## Slide 8: Layerweaver: Maximizing NPU Resource Utilization
Layerweaver efficiently interweaves layer-wise execution of multiple DNNs to maximize resource utilization and throughput of NPU by utilizing a lightweight scheduler
Proposes a lightweight scheduling algorithm that efficiently interleaves multiple DNNs
Carefully considers on-chip memory size, output forwarding, and starvation
Does not require special hardware support to be readily applicable to existing NPUs
Achieves high throughput and nearly-full resource utilization on 16 pairs of DNN models, various inference scenarios, and NPUs

## Slide 9: Presentation Outline
Resource Underutilization Problem of DNN Accelerators
Layerweaver: Maximizing Temporal Resource Utilization
Building Efficient DNN Serving System w/ Layerweaver
  Overview of Greedy Scheduler w/ Service Requests
  Calculation of Compute and Memory Idle Time
  Layer Selection Process
Evaluation
Conclusions

## Slide 10: Overview of Layerweaver Serving System
Assuming a frontend load balancer that distributes a mix of both memory- and compute-intensive requests at pre-determined rates to worker nodes
Host processor triggers the greedy, layer-wise scheduler when a schedulable batch is formed
Greedy Scheduler accepts requests and adds them to the (scheduling) candidate group
  Then the scheduler selects the next layer to schedule from this candidate group leading to the least idle time in compute/memory resources
Off-chip DRAM
Host Processor
NPU
Greedy
Scheduler
Commands
Finish any?
PCIe
Request Q
Other Workers
M2
C2
C1
M1
Comp-intensive
Mem-intensive
Load
Balancer
Feedback
Interweaved
Inst. Streams
(Appended)
NPU Core
Global Buf.
Request Streams

## Slide 11: Light-weight Scheduling Algorithm of Layerweaver
Observation: To minimize idle time, keep a proper decoupling distance
Def. Decoupling distance: Time difference btw. the last fetch completion (Tm) and computation finish (Tc)
  Too long decoupling distance: Potential Memory Idle Time
  Too short decoupling distance: Potential Compute Idle Time
Time
C1
C1
C2
C2
Compute
Memory
Tm
Tc
Time
C1
C1
C2
C2
Compute
Memory
Tm
Tc
* Dependence graph of input & output activation is omitted
On-chip memory is full,
Memory Idle Time
Long decoupling
distance
Short decoupling
distance
Input data not yet prepared,
Compute Idle Time
…

## Slide 12: Light-weight Scheduling Algorithm of Layerweaver
Calculating Compute Idle Time
  When too short decoupling distance exists, there could be Compute Idle Time
  Before starting computation of B1, the input data of B1 should be prepared
A1
A1
Compute
Memory
Compute Idle Time = 0
A2
A2
Mem. Time
Decoupling distance
A1
A1
Compute
Memory
Decoupling distance
B1
B1
Compute Idle Time = Mem. Time – Decoupling distance
Mem. Time

## Slide 13: Light-weight Scheduling Algorithm of Layerweaver
A1
Compute
Memory
A1
Calculating Memory Idle Time
  When too large decoupling distance exists, there could be Memory Idle Time
  Free on-chip buffer size for now = 600 KB
Time to fetch 600 KB (6us)
A2
= 600 KB / 100 GB/s (Mem. BW) = 6 us
Memory Idle Time = 0
Decoupling distance

## Slide 14: Light-weight Scheduling Algorithm of Layerweaver
Time to fetch 600 KB (6us)
A1
A1
Compute
Memory
B1
Calculating Memory Idle Time
  When too large decoupling distance exists, there could be Memory Idle Time
  Free on-chip buffer size for now = 600 KB
B1
Memory Idle Time = Decoupling distance – 6 us
= 600 KB / 100 GB/s (Mem. BW) = 6 us
Buffer size limit is met

## Slide 15: Light-weight Scheduling Algorithm of Layerweaver
Calculating Memory Idle Time (Cont’d)
  Some models have Inherent Memory Idle Time, which cannot be removed by scheduling
  To prevent additional memory idle time, keep minimum decoupling distance
A1
A1
B3
…
A1
A1
Compute
Memory
…
Time for “total” on-chip buffer size
available for prefetch
Inherent Memory Idle Time
(Scheduling cannot remove this)
Very large decoupling distance
The same amount available for prefetch
Increased Memory Idle Time caused by
B3 and its increased decoupling distance

## Slide 16: Light-weight Scheduling Algorithm of Layerweaver
Host Processor
Greedy Scheduler
Request Q
C1
M1
Comp-intensive
Mem-intensive
C2
Layer Selection
  Detailed formal descriptions about every idle time case are available in our paper
  After exactly calculates the idle time of “each layers in progress” from K candidate requests ~ O(k)
  Select the layer that incurs minimum memory and compute idle time, and repeat for N layers ~ O(kN)
Model | Progress
C0 | -
M1 | -
C2 | -
Idle Time
20
5
0
To NPU
Selected layer after scheduling
Layer 1
Candidate Group

## Slide 17: Presentation Outline
Resource Underutilization Problem of DNN Accelerators
Layerweaver: Maximizing Temporal Resource Utilization
Building Efficient DNN Serving System w/ Layerweaver
  Overview of Greedy Scheduler w/ Service Requests
  Calculation of Compute and Memory Idle Time
  Layer Selection Process
Evaluation
Conclusions

## Slide 18: Evaluation Methodology & Inference Scenario
Evaluation Scenario: Single- / Multi-batch Streams (Extended Single-stream in MLPerf [1])
Accelerators: Memory-centric (Google TPUv3 style) & Compute-centric (Intel NNP-I style) NPUs
Baseline Strategy: Memory-only / Compute-only / Fair / AI-MT [2]
Metrics: Normalized System Throughput (STP), Time Utilization (%)
[1] Reddi et al., ”MLPerf Inference Benchmark”, ISCA ’20
[2] Baek et al., “A Multi-Neural Network Acceleration Architecture”, ISCA ’20
Input Timeline for Multi-Batch Streams (# of Streams = 2)
ti j = Processing time for jth query of request i streams
t10
t11
t12
t00
t01
t03
t02
…
…
N
M
Batch size

## Slide 19: Performance Evaluation (System Throughput)
Scenario: Single-Batch Streams (# of Streams = 2) on TPUv3-style NPU
Layerweaver: 60.1% throughput increase over the baseline (Fair)
Against AI-MT: Layerweaver shows 21.6% higher geomean STP than AI-MT
  AI-MT: State-of-the-art time-multiplexed DNN multi-tasking technique
  Layerweaver estimates the resource idle time more precisely than AI-MT based on a simple heuristic
For various Multi-Batch Streams configurations, Layerweaver outperforms all the other schemes
Single-Batch Streams (# of Streams = 2)
Multi-Batch Streams (# of Streams = 2, Geomean)
Memory-centric NPU
Compute-centric NPU
Smaller benefits w/
biased config.
Batch Size
Batch Size

## Slide 20: Overall NPU Resource Utilization
Evaluation Scenario: Single-Batch Streams (# of Streams = 2) w/ TPUv3-style NPU
Layerweaver almost fully (Geomean 99.7% / 91.3% for Compute / Memory) utilizes active cycles
ResNeXt causes Inherent Memory Idle Time and about 29-31% drop in memory active cycles (Red box)
  As we discussed this drop is not attributed to scheduling decisions
Memory- or Compute-only suffers severely from either compute or memory bandwidth underutilization
AI-MT shows sub-optimal results due to imprecise estimation of resource idle time
Compute (PE) Active Cycles
Memory (DRAM) Active Cycles

## Slide 21: Scheduling Overhead
Layerweaver scheduler has O(kN) complexity
  k: # of candidate models, N: total # of layers to schedule
Carefully modeled scheduling overhead on a host processor
  Intel i7-7700K CPU @ 4.20GHz
  Greedy Scheduler Throughput is 15 layers / us
Compared to the single batch-1 layer latency which ranges from 4.7us to 221us
  The scheduling overhead is negligible
  Also, scheduling happens off-critical path most of the time using host CPU
Thus, Layerweaver can flexibly support dynamically-changing request patterns at runtime

## Slide 22: Layerweaver: Maximizing NPU Resource Utilization
Proposes a lightweight scheduling algorithm that efficiently interleaves multiple DNNs
Carefully considers on-chip memory size, output forwarding, and starvation
Does not require special hardware support to be readily applicable to existing NPUs
Achieves high throughput and nearly-full resource utilization on 16 pairs of DNN models, various inference scenarios, and NPUs
Layerweaver efficiently interweaves layer-wise execution of multiple DNNs to maximize resource utilization and throughput of NPU by utilizing a lightweight scheduler

## Slide 23
Layerweaver: Maximizing Resource Utilization of Neural Processing Units via Layer-Wise Scheduling
Young H. Oh† , Seonghak Kim*, Yunho Jin*, Sam Son*, Jonghyun Bae* Jongsung Lee*, Yeonhong Park*, Dong Uk Kim*, Tae Jun Ham*, Jae W. Lee*
*Seoul National University
†Sungkyunkwan University
Author Contact Info: younghwan@skku.edu
The 27th IEEE International Symposium on High-Performance Computer Architecture